## Slide 1: Machine Instructions and Programs

## Slide 2
Machine Instructions and Programs
Memory Locations and Ad dress, Byte addressability, Big-endian and Little-endian assignments, Word Alignment, Accessing Numbers, Characters and Character strings, memory Operation, Instruction and Instruction Sequencing, Register Transfer Notation, Assembly Language Notation.

## Slide 3: Objectives
Machine instructions and program execution, including branching and subroutine call and return operations.
Addressing methods for accessing register and memory operands.
Assembly language for representing machine instructions, data, and programs.
Program-controlled Input/Output operations.

## Slide 4: Memory Locations, Addresses, and Operations

## Slide 5: Memory Location, Addresses, and Operation
Memory consists of many millions of storage cells, each of which can store 1 bit.
Data is usually accessed in n-bit groups. n is called word length.
second word
first word
Figure Memory words.
last word
i
th word
•
•
•
•
•
•
N bits

## Slide 6: Memory Location, Addresses, and Operation
32-bit word length example
(b) Four characters
character
character
character
character
(a) A signed integer
Sign bit:
for positive numbers
for negative numbers
ASCII
ASCII
ASCII
ASCII
32 bits
8 bits
8 bits
8 bits
8 bits
b
31
b
30
b
1
b
0
b
31
0
=
b
31
1
=
•
•
•

## Slide 7: Memory Location, Addresses, and Operation
To retrieve information from memory, either for one word or one byte (8-bit), addresses for each location are needed.
A k-bit address memory has 2k memory locations, namely 0 – 2k-1, called memory space.
24-bit memory: 224 = 16,777,216 = 16M (1M=220)
32-bit memory: 232 = 4G (1G=230)
1K(kilo)=210
1T(tera)=240

## Slide 8: Memory Location, Addresses, and Operation
It is impractical to assign distinct addresses to individual bit locations in the memory.
The most practical assignment is to have successive addresses refer to successive byte locations in the memory – byte-addressable memory.
Byte locations have addresses 0, 1, 2, … If word length is 32 bits, they successive words are located at addresses 0, 4, 8,…

## Slide 9: Big-Endian and Little-Endian Assignments
Big-Endian: lower byte addresses are used for the most significant bytes of the word
Little-Endian: opposite ordering. lower byte addresses are used for the less significant bytes of the word

## Slide 10
2
k
4
-
2
k
4
-
0
0
4
4
2
k
1
-
2
k
2
-
2
k
3
-
2
k
4
-
3
2
1
0
7
6
5
4
•
•
•
2
k
4
-
2
k
3
-
2
k
2
-
2
k
1
-
0
1
2
3
4
5
6
7
•
•
•
Address Byte Address Address Byte Addess
(a) Big-endian assignment
(b) Little-endian assignment
Figure Byte and word addressing.

## Slide 11: Memory Location, Addresses, and Operation
Address ordering of bytes
Word alignment
  Words are said to be aligned in memory if they begin at a byte addr. that is a multiple of the num of bytes in a word.
    16-bit word: word addresses: 0, 2, 4,….
    32-bit word: word addresses: 0, 4, 8,….
    64-bit word: word addresses: 0, 8,16,….
Access numbers, characters, and character strings

## Slide 12: Memory Operation
Load (or Read or Fetch)
Copy the content. The memory content doesn’t change.
Address – Load
Registers can be used
Store (or Write)
Overwrite the content in memory
Address and Data – Store
Registers can be used

## Slide 13: Instruction and Instruction Sequencing

## Slide 14: “Must-Perform” Operations
Data transfers between the memory and the processor registers
Arithmetic and logic operations on data
Program sequencing and control
I/O transfers

## Slide 15: CPU Organization
Single Accumulator
  Result usually goes to the Accumulator
  Accumulator has to be saved to memory quite often
General Register
  Registers hold operands thus reduce memory traffic
  Register bookkeeping
Stack
  Operands and result are always in the stack

## Slide 16: Register Transfer Notation
Identify a location by a symbolic name standing for its hardware binary address (LOC, R0,…)
Contents of a location are denoted by placing square brackets around the name of the location (R1←[LOC], R3 ←[R1]+[R2])
Register Transfer Notation (RTN)

## Slide 17: Assembly Language Notation
We consider different types of machine
Three address machine
Two address machine
One address machine
Zero address machine

## Slide 18
Three address Instructions:
ADD R1, R2, R3; R3  [R1] + [R2]
SUB R1, R2, R3; R3 [R1] – [R2]
MUL R1, R2, R3; R3 [R1] * [R2]
DIV R1, R2, R3; R3 [R1] / [R2]
LOAD M, R ; R  [ M ]
STORE R, M ; [M]  [R]

## Slide 19
Example: Evaluate the following expression x=(A+B)  (C+D) by three-Address
  ADD A, B, R1 ; R1 ← M[A] + M[B]
  ADD C, D, R2 ; R2 ← M[C] + M[D]
  MUL R1, R2, X ; M[X] ← R1  R2

## Slide 20
Two address Instruction Format:
ADD R1, R2; R2 [R2] +[R1]
SUB R1, R2; R2 [R2] – [R1]
MUL R1, R2; R2  [R2] * [R1]
DIV R1, R2; R2 [R2] / [R1]
LOAD M, R ; R [ M ]
STORE R, M ; [M]  R

## Slide 21
One address Instruction format:
In One address instruction machine, one register is assumed to be accumulator. Accumulator is shown as Acc. in the instruction.
ADD A; [Acc]  [Acc] + M[A]
SUB A; [Acc] [Acc] - M[A]
MUL A [Acc] [Acc] * M[A]
DIV A [Acc ][Acc ]/ M[A]
LOAD A [Acc] M[A]
STORE A M[A] [ Acc]

## Slide 22
Example: Evaluate (A+B)  (C+D)
One-Address
  LOAD A ; ACc ← M[A]
  ADD B ; ACc← ACc + M[B]
  STORE T ; M[T] ← ACc
  LOAD C ; ACc ← M[C]
  ADD D ; ACc ← ACc + M[D]
  MUL T ; ACc ← ACc  M[T]
  STORE X ; M[X] ← ACc

## Slide 23
Zero Address Instructions machine
It is also called stack machine. In this machine, the operation takes place on the top of the stack. The procedure is that the arithmetic operation that takes place on the top of the stack and one location below it.
ADD ; TOS[STACK] = TOS[STACK] + TOS-1[STACK-1]
SUB ; TOS[STACK] = TOS[STACK] - TOS-1[STACK-1]
MUL ; TOS[STACK] = TOS[STACK] * TOS-1[STACK-1]
DIV ; TOS[STACK] = TOS[STACK] / TOS-1[STACK-1]
PUSH A; TOS[STACK] = A
POP A ; A = TOS[STACK]

## Slide 24: Instruction Formats
Example: Evaluate (A+B)  (C+D)
Zero-Address
  PUSH A ; TOS ← A
  PUSH B ; TOS ← B
  ADD ; TOS ← (A + B)
  PUSH C ; TOS ← C
  PUSH D ; TOS ← D
  ADD ; TOS ← (C + D)
  MUL ; TOS ← (C+D)(A+B)
  POP X ; M[X] ← TOS

## Slide 25: Using Registers
Registers are faster
Shorter instructions
  The number of registers is smaller (e.g. 32 registers need 5 bits)
Potential speedup
Minimize the frequency with which data is moved back and forth between the memory and processor registers.

## Slide 26: UNIT II
Chapter 2

## Slide 27: Instruction Execution and Straight-Line Sequencing
Begin execution here
Address Contents
Move R0, C
Move A, R0
Add B, R0
i
+ 8
i
C
B
A
i
+ 4
Figure A program for C ¬ [A] + [B].
Three – Instruction program segment
Data for the program

## Slide 28
Program Counter: Contains the address of instruction to be executed next.
Assumptions:
  - One memory operand per instruction
  - 32-bit word length
  - Memory is byte addressable
  Full memory address can be directly specified in a single-word instruction
Two-phase procedure
Instruction fetch IR
Instruction execute

## Slide 29: Branching
i | Move NUM1 , R0
i+4 | ADD NUM2, R0
i+8 | ADD NUM3, R0
 | .
 | .
 | .
i+4n-4 | ADD NUMn, R0
i+4n | Move R0, SUM
 | .
 | .
 | .
Sum | 
NUM1 | 
NUM2 | 
NUMn | 
Program to add ‘n’ nums which is stored from the location NUM1 to NUMn. Store the sum in the memory location SUM.
This program does a routine operation of adding from the consecutive locations. Can this be optimized?

## Slide 30: Branching
n
Using a loop to add n numbers.
loop
Program
MOVE N, R1
CLEAR R0
Determine the address of “Next number and add it to R0
Decrement R1
Branch > 0 LOOP
Move R0, SUM
NUM n
NUM2
NUM1
N
SUM
.
.
.

## Slide 31: Condition Codes
Condition code flags
Condition code register / status register
N (negative)
Z (zero)
V (overflow)
C (carry)
Different instructions affect different flags

## Slide 32: Conditional Branch Instructions
Example:
  A: 1 1 1 1 0 0 0 0
  B: 0 0 0 1 0 1 0 0
A: 1 1 1 1 0 0 0 0
+(−B): 1 1 1 0 1 1 0 0
1 1 0 1 1 1 0 0
C = 1
S = 1
V = 0
Z = 0

## Slide 33: Status Bits
ALU
V
Z
S
C
Zero Check
Cn
Cn-1
Fn-1
A
B
F

## Slide 34: Addressing Modes

## Slide 35: Generating Memory Addresses
Addressing mode is a means of finding the different ways in which the location of an operand is specified in the instruction.
How to specify the address of branch target?
Can we give the memory operand address directly in a single Add instruction in the loop?
Use a register to hold the address of NUM1; then increment by 4 on each pass through the loop.

## Slide 36
The different types of addressing modes are –
Register addressing mode
Register Indirect addressing mode
Absolute/Direct addressing mode
Immediate addressing mode
Indirect addressing mode
Indexed addressing mode
Base with index and offset
Relative addressing mode
Autoincrement mode
Autodecrement mode

## Slide 37
Register Addressing mode:
In this addressing mode, the operand is the contents of a processor register. The name of the register is in the instruction.
Example: MOVE R1, R2

## Slide 38
Absolute/ Direct Addressing mode:
In Absolute addressing mode, the address of the operand is given in the instruction itself.
Example: MOVE LOC, R0
Immediate Addressing mode:
In this addressing mode, the data itself is immediately given in the instruction itself.
Example: MOV 200immediate, R0
MOV #200, R0

## Slide 39
Indirect addressing mode:
There are two Indirect addressing mode.
(a) Register Indirect addressing mode:
The effective address of the memory operand is the contents of a register which is mentioned in the instruction. It means the memory is accessed by using the address available in the register.
Example: MOVE [R2], R0
ADD (R1),R0
Here the register R2 contains the memory address. The data is moved from the memory location pointed by register R2 and moved to register R2

## Slide 40
(b) Memory Indirect Addressing Mode:
In this addressing mode, the address of the operand is available in the memory.
AR = 101
100
101
102
103
104
Memory
0 1 0 4
1 1 0 A
MOV [AR], R0
Drawback:
Mem is accessed twice to get an operand so not well suited
110A
R0

## Slide 41
Implied Addressing mode
In this addressing mode, it is understood that the operand is on the register.
Example: ADD
In zero addressing mode the Top of the Stack is understood.

## Slide 42
Autoincrement Addressing Mode:
In this mode the effective address of the operand id the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
(Ri)+
Example: Add (R2)+, R0
Contents of memory pointed by R2 is added to contents of R0 and the result is stored in register R0. After the addition operation the register R2 is increment by the operand size.
Note: If the operand is byte data then the increment is one.
If the operand is 16bits then the increment is 2
If the operand is 32 bits then the increment is 4.

## Slide 43
Auto decrement Addressing Mode:
In this mode the effective address mode, the content of a register specified in the instruction are first automatically decremented and are then used as the effective address of the operand.
- (Ri)
The actions performed by the Autoincrement and Autodecrement addressing mode can be achieved by using two instructions. One to access the operand and the other to increment or decrement the register that contains the operand.

## Slide 44
Indexed Addressing Mode:
In this addressing mode the effective address of the operand is generated by adding a constant value to the contents of a register.
  EA = X+[Ri]
100
101
102
103
104
Memory
R2 = 100
1 1 0 A
X1 = 2
+
X (Ri)
Where X denotes the constant value contained in the instruction and Ri is the name of the register involved.
Example:Add X1(R2),R0
If X1 =2, and R2=100 then the figure shows that the contents of memory 102 is accessed to add with R0 and stored in R0

## Slide 45
100
101
102
103
104
Memory
0
1
2
Relative Addressing Mode
In this addressing mode, the address of the operand is calculated relative to the PC.
AR = 100
1 1 0 A
PC = 2
+
Program
Data
Could be Positive or Negative (2’s Complement)
Example:
Branch > 0 LOOP
The effective address of the operand is calculated with respect to PC
  EA = PC + Relative Addr

## Slide 46
Base Register addressing mode
  EA = Base Register + Relative Addr
  BR = Base Register; AR = Relative Address
100
101
102
103
104
Memory
BR = 100
0 0 0 A
AR = 2
+
Could be Positive or Negative (2’s Complement)
Usually points to the beginning of an array
0 0 0 5
0 0 1 2
0 1 0 7
0 0 5 9
In this addressing mode the base register contents is considered to be a part of the
address. This value is added to the Relative address to calculate the effective address.

## Slide 47
The different ways in which the location of an operand is specified in an instruction are referred to as addressing modes.
Name
Assembler
syntax
Addressing
function
Immediate
#V
alue
Op
erand
=
V
alue
Register
R
i
EA
=
R
i
Absolute
(Direct)
LOC
EA
=
LOC
Indirect
(R
i
)
EA
=
[R
i
]
(LOC)
EA
=
[LOC]
Index
X(R
i
)
EA
=
[R
i
]
+
X
Base
with
index
(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
Base
with
index
X(R
i
,R
j
)
EA
=
[R
i
]
+
[R
j
]
+
X
and
offset
Relative
X(PC)
EA
=
[PC]
+
X
Autoincremen
t
(R
i
)+
EA
=
[R
i
]
;
Incremen
t
R
i
Autodecrement
(R
i
)
Decremen
t
R
i
;
EA
=
[R
i
]


## Slide 48
Immediate data can be either in binary, decimal or Hexadecimal. To identify each of the number system a symbol is prefix is used. It is shown in the table.
Number | Number System | Prefix symbol | Example
32 | Decimal |  | Add #5, R6
10101110 | Binary | % | MOV #%10101110
5D | Hexa decimal | $ | MOV $#5D, R5

## Slide 49: Assembly Language

## Slide 50
Programs written using 0’s and 1’s are machine instructions.
Machine instructions are difficult to write or to read. Hence mnemonic are used to represent the operations such as
ADD
SUM
MOVE
Similarly, R3 is the notation used to refer to register 3.
A complete set of such symbolic names and rules for their use constitute a programming language, generally referred to as assembly language.
The set of rules for using the mnemonics is the specification of complete instruction and program is called the syntax of the language

## Slide 51
Assembler system program is stored in memory.
User written assembly level program is entered in primary memory.
When assembled, the assembly level user program is converted to machine level program and stored in sequential memory location.
Assembler has a standard with mnemonic followed by operand or operands. There are delimiters between mnemonic, register R1 and memory ‘SUM’ in the example shown below.
Example: Move R1, SUM
Assembler
Source Program
Object Program

## Slide 52
Assembler needs some information to understand and interpret what user wants. These extra information that is provided to make Assembler understand is called assembler directive.
Assembler directives:
Assembler directives are the instructions to the assembler that specifies information needed to translate the source program into the object program. Assembler directives are not translated to object code by the assembler. Some of them are discussed below.
EQUATE: SUM EQU 100
It informs the assembler that SUM should be replaced by the value 200, wherever it appears in the program

## Slide 53
Origin: It tells the assembler program where in the memory to place the block that follows.
Example: ORIGIN 198
DATAWORD 64
The data that is following the ORIGIN, 198 is the location from where the next data is being stored.
DATAWORD: It is an assembler directive stating that the data that is following it is 16 bits data. In the above example, the memory location following ORIGIN location 198 a memory of 16 bits are used to store the data.
It is possible to use a variable name before the DATAWORD indicating that the variable name mentioned is 16 bits.
Address | Data/Opcode
199 | 64

## Slide 54
END: The end directive is used to tell the assembler that the program has ended. There are no more instructions following this statement for assembly.
Usually, following the END statement a variable is used which is the label of the start of the program. The label points to the address of the location at which execution of the program is to begin.
Assembly Language Format:
Assembly language program is usually written in a specific format to enable the assembler to tokenise each token for assembling the program. However it is also convenient for the user the read the assembly program.
There are four fields separated by appropriate delimiters.
LABEL OPERATION OPERANDS COMMENTS

## Slide 55
Typically, one or more blank characters are used to separate the fields.
Label: It is an optional field. A name is associated with the memory address is mentioned in this field.
Operation Field: This field contains Operation code mnemonic of the desired instruction.
Operand Field: It is an optional field. If the Operation code requires one of more operand it is mentioned in this field.
Comments: It is optional field. It is used for documentation of the program. The assembler will ignore this field.

## Slide 57: Stacks and Queues
Control and info linkage b/w main program and subroutine is through stacks
LIFO/FILO data structure

## Slide 58: Stack operations
PUSH
Subtract #4,SP
Move NEWITEM,(SP)
POP
MOVE (SP),ITEM
ADD #4,SP

## Slide 59: Effect of PUSH and POP operation

## Slide 60: Use of Auto decrement and Increment for PUSH and POP operation
PUSH
MOVE NEWITEM, -(SP)
POP
MOVE (SP)+, ITEM

## Slide 61: SAFE POP operation
Compare #2000,SP
Branch>0 EMPTYERROR
Move (SP)+,ITEM

## Slide 62: SAFE PUSH operation
Compare #1500,SP
Branch<=0 FULLERROR
Move NEWITEM,-(SP)

## Slide 63: Queues
FIFO
Difference b/w Stack and Queue
stack uses single pointer and queue two

## Slide 64: SUBROUTINES
Saves space
Subroutine call
Subroutine return
Subroutine linkage method(using linkage register)

## Slide 65: SUBROUTINES
Call instruction is a special branch instruction that performs following operations
Store the contents of the PC in the linkage register
Branch to target address specified by the instn
Return instruction is a special branch instrn that performs following operations
Branch to the address contained in the link register

## Slide 66: SUBROUTINES

## Slide 67: Subroutine nesting and Processor stack
Subroutine call another subroutine
Single link register is not sufficient
Stored on processor stack

## Slide 68
END

## Slide 69
Instruction Set
The instruction set of a computer is machine dependent. It is required to know the instruction set to write a program. Instruction set can be grouped based on the type of the operation. The different group are –
Data Transfer group
Arithmetic and logic group
Branch transfer group
Machine group
Data Transfer Group:
Data transfer group of instructions consists of all the data transfer from register to register, register to memory, memory to registry and input output instructions. There is no instruction to move data from memory to memory transfer.

## Slide 70
Move R1, R2 ; Register addressing mode
Move #5, R3 ; Immediate addressing mode
Move (R1), R2 ; Register indirect addressing mode
Move –(R5), R0; Auto decrement addressing mode
Move X(R2), R1; Index addressing mode
Movemultiple (R0-R3), -SP ; This is an instruction where multiple registers are moved on the top of the stack. Before the contents of register is saved on the top of the stack, the contents of the stack pointer is decremented by two. The process continues till all the register is saved on the top of the stack.
Movemultiple(SP)+, (R0-R3) : The data from the top of the stack is moved to the registers mentioned in the instruction.

## Slide 71
Input Data Transfer Instruction:
Data from input devices can be accessed using MoveByte instruction. Before moving the data from the input device, which is much slower than the CPU, the program checks whether the device has made the data available by seeing a flag SIN. If the SIN flag is 0, the data is not ready and if the SIN flag is 1, then the data is available in I/O area DATAIN and the data can be readt
READWAIT BRANCH to READWAIT if SIN=0
MOVEByte DATAIN, R1
Output Data Transfer Instruction:
Data can be sent out of the processor much faster than the device can accept. To make sure that data is not lost, it is

## Slide 72
R 0equired to check whether the device is ready to receive data. This is being done by looking into a flag called Sout. If Sout = 0 then the device is not ready. If Sout =1, then device is ready to receive the data. It is required to write an instruction to make the program check Sout flag and wait there till the device is ready to accept. Once the device is ready send the data to DATAOUT register.
WriteWait Branch WriteWait if Sout = 0
Movebyte R1, DATAOUT
MOVE (R1, R2), R3 ; This is an instruction which is multi-dimensional addressing mode. The contents of R1 and R2 are added to access the data from memory and store the result in register R3. R1 is for one of the index and R2 is for the second index in two dimensional data access.

## Slide 73
Arithmetic and Logical group:
Arithmetic instructions consists of Addition, Subtraction, Multiplication and division instructions.
Addition:
ADD R1, R2; Register addressing mode
ADD #6, R3; Immediate addressing mode
ADD (R4), R2 ; Register indirect addressing mode
ADD X(R5), R4; Index addressing mode
ADD (R1, R3), R8; Multi index addressing mode
INCREMENT R5; R5 = R5 + 1

## Slide 74
Subtraction:
SUB R1, R2; Register addressing mode
SUB #6, R3; Immediate addressing mode
SUB (R4), R2 ; Register indirect addressing mode
SUB X(R5), R4; Index addressing mode
SUB (R1, R3), R8; Multi index addressing mode
Decrement R1; R1=R1-1

## Slide 75
Multiplication:
MUL R1, R2; Register addressing mode
MUL #6, R3; Immediate addressing mode
MUL (R4), R2 ; Register indirect addressing mode
MUL X(R5), R4; Index addressing mode
MUL (R1, R3), R8; Multi index addressing mode

## Slide 76
Division:
DIV R1, R2; Register addressing mode
DIV #6, R3; Immediate addressing mode
DIV (R4), R2 ; Register indirect addressing mode
DIV X(R5), R4; Index addressing mode
DIV (R1, R3), R8; Multi index addressing mode

## Slide 77: Input Output Organization

## Slide 78: Accessing I/O devices - A Single bus structure
Bus
I/O de
vice 1
I/O de
vice
n
Processor
Memory

## Slide 79: Accessing I/O devices
Memory mapped IO
IO devices and memory share the same address space.
Move DATAIN,R0
Move R0, DATAOUT
DATAIN and DATAOUT are buffers
I/O devices and the memory may have different address spaces:
Special instructions to transfer data to and from I/O devices.

## Slide 80: Accessing I/O devices
I/O Interface for an input device
I/O
int
erface
decoder
Address
Data and
status registers
Control
circuits
Input device
Bus
Address lines
Data lines
Control lines

## Slide 81: Registers in keyboard and display Interfaces

## Slide 82: Program to read a line from Keyboard and stores in memory buffer and echoes on display
Figure 4.4

## Slide 83: Program controlled IO
Program in fig 4.4
Processor repeatedly checks status flag to achieve synchronization b/w processor and IO device.
  Processor polls the I/O device.
  Two other mechanisms used for synchronizing data transfers between the processor and memory:
  Interrupts
  DMA

## Slide 84: INTERRUPTS
Drawback of programmed IO
processor time is wasted in waiting for IO device without doing useful processing.
Waiting period can be avoided by allowing IO devices to notify the processor when they are ready
Done through Hardware Interrupts
Interrupt Service Routine(PRINT function)
Interrupt latency(Time b/w receipt of interrupt req and start of execution of interrupt service routine.
here
Interrupt
occurs
M
i
2
1
i
1
+
Transfer of control through interrupts
Program 1 Program 2
COMPUTE routine PRINT routine
Interrupts save PC and status register
Some interrupts save the registers some not

## Slide 85: Interrupt Hardware
Single interrupt line is used to serve n devices
Closing of switches makes voltage to drop to 0 and INTR received by processor will goto 1
If all switches are open voltage will be vdd
INTR=INTR1+INTR2+INTR3+………+INTRn

## Slide 86: Interrupts (contd..)
Treatment of an interrupt-service routine is very similar to that of a subroutine.
However there are significant differences:
  A subroutine performs a task that is required by the calling program.
  Interrupt-service routine may not have anything in common with the program it interrupts.
  Interrupt-service routine and the program that it interrupts may belong to different users.
  As a result, before branching to the interrupt-service routine, not only the PC, but other information such as condition code flags, and processor registers used by both the interrupted program and the interrupt service routine must be stored.
  This will enable the interrupted program to resume execution upon return from interrupt service routine.

## Slide 87: Interrupts (contd..)
Saving and restoring information can be done automatically by the processor or explicitly by program instructions.
Saving and restoring registers involves memory transfers:
  Increases the total execution time.
  Increases the delay between the time an interrupt request is received, and the start of execution of the interrupt-service routine. This delay is called interrupt latency.
In order to reduce the interrupt latency, most processors save only the minimal amount of information:
  This minimal amount of information includes Program Counter and processor status registers.
Any additional information that must be saved, must be saved explicitly by the program instructions at the beginning of the interrupt service routine.

## Slide 88: Interrupts (contd..)
When a processor receives an interrupt-request, it must branch to the interrupt service routine.
It must also inform the device that it has recognized the interrupt request.
This can be accomplished in two ways:
  Some processors have an explicit interrupt-acknowledge control signal for this purpose.
  In other cases, the data transfer that takes place between the device and the processor can be used to inform the device.

## Slide 89: Interrupts (contd..)
Interrupt-requests interrupt the execution of a program, and may alter the intended sequence of events:
  Sometimes such alterations may be undesirable, and must not be allowed.
  For example, the processor may not want to be interrupted by the same device while executing its interrupt-service routine.
Processors generally provide the ability to enable and disable such interruptions as desired.
One simple way is to provide machine instructions such as Interrupt-enable and Interrupt-disable for this purpose.
To avoid interruption by the same device during the execution of an interrupt service routine:
  First instruction of an interrupt service routine can be Interrupt-disable.
  Last instruction of an interrupt service routine can be Interrupt-enable.

## Slide 91: How to avoid successive interruptions
Enable and Disable instruction in beginning and ending of ISR
Using PS register enable bit
Edge triggered :
Interrupt request line of processor will respond to interrupt handling circuit for leading edge of the signal.
Processor will receive only one request regardless of how long the line is activated.

## Slide 92: Enabling and Disabling Interrupts- Sequence of actions
The device raises an interrupt request
The processor interrupts the program currently being executed
Interrupts are disabled by changing the control bits in PS.
The device is informed that its request has been recognized and in response , it deactivates the interrupt request signal
The action requested by the interrupt service routine
Interrupts are enabled and execution of the interrupted program is resumed.

## Slide 93: Handling Multiple Interrupts
Multiple I/O devices may be connected –HOW TO ADDRESS
How does the processor know which device has generated an interrupt?
How does the processor know which interrupt service routine needs to be executed?
When the processor is executing an interrupt service routine for one device, can other device interrupt the processor?
If two interrupt-requests are received simultaneously, then how to break the tie?

## Slide 94: How to recognize the interrupted device
ISR Polls the devices connected.
If the IRQ bit=1 then serves the device
Polling mechanism is easy, but time consuming to query the status bits of all the I/O devices connected to the bus.

## Slide 95: Vectored Interrupts
Device identifies itself to the processor by sending a code.
CODE is starting addr(interrupt vector) of ISR(4 to 8 bits code length) but need not be ISR
IVPC
INTR(Device activates when it is ready with interrupt)
INTA(Processor activates when it is ready to receive INT)

## Slide 96: Interrupt Nesting- Priority
I/O devices are organized in a priority structure:
  An interrupt request from a high-priority device is accepted while the processor is executing the interrupt service routine of a low priority device.
A priority level is assigned to a processor that can be changed under program control.
  Priority level of a processor is the priority of the program that is currently being executed.
  When the processor starts executing the interrupt service routine of a device, its priority is raised to that of the device.
  If the device sending an interrupt request has a higher priority than the processor, the processor accepts the interrupt request.
Notes: Repeat that multiple I/O devices may be connected to the processor. These multiple I/O devices may be organized according a certain priority. When the processor is servicing an interrupt from a device, only devices which have higher priority can interrupt the processor. That is, only devices which have higher priority can interrupt the processing of the ISR of the device of lower priority.
In order to implement this scheme, a priority level is assigned to a processor. This priority level can be changed under program control or it depends on which program is currently being executed by the processor. That is, the priority of the processor is the priority of the program that the processor is currently executing. When the processor receives an interrupt request from a device, and starts executing the ISR of that device, its priority is raised to that of the device. Now, if another device wants to interrupt the processor, then it is allowed to do so, only if its priority is higher than the priority of the processor which is set to the priority of the ISR of the device.

## Slide 97: Multiple Priority Levels
Priority arbitration
Device 1
Device 2
Device
p
Processor
INTA1
I
N
T
R
1
I
N
T
R
p
INTA
p
Each device has a separate interrupt-request and interrupt-acknowledge line.
Each interrupt-request line is assigned a different priority level.
Interrupt requests received over these lines are sent to a priority arbitration circuit
in the processor.
If the interrupt request has a higher priority level than the priority of the processor,
then the request is accepted.

## Slide 98: Simultaneous Requests-No separate INTR line
Which interrupt request does the processor accept if it receives interrupt requests from two or more devices simultaneously?.
If the I/O devices are organized in a priority structure, the processor accepts the interrupt request from a device with higher priority.
  Each device has its own interrupt request and interrupt acknowledge line.
  A different priority level is assigned to the interrupt request line of each device.
However, if the devices share an interrupt request line, then how does the processor decide which interrupt request to accept?

## Slide 99: Daisy chain
Polling
Vectored Interrupt
Daisy chain
Processor
Device 2
I
N
T
R
INTA
Device
n
Device 1

## Slide 100: Arrangement of Priority Groups
Device
Device
circuit
Priority arbitration
Processor
Device
Device
I
N
T
R
1
I
N
T
R
p
INTA1
INTA
p

## Slide 102: Controlling Device Requests
Devices used in a program are allowed to generate interrupt requests.
To control which devices are allowed to generate interrupt requests, the interface circuit of each I/O device has an interrupt-enable bit.
  If the interrupt-enable bit in the device interface is set to 1, then the device is allowed to generate an interrupt-request.
Interrupt-enable bit in the device’s interface circuit determines whether the device is allowed to generate an interrupt request.
If DEN(Device)=1DIRQ(Processor) , KEN=1KIRQ

## Slide 103: Using interrupts to read line of characters

## Slide 104: Exceptions
  Error in the data stored.
  Error during the execution of an instruction.
Types of exceptions are:
  Recovery from errors
  Debugging
  Privilege exception
Recovery from exception Exception service routine
Divide by zero, un recognized OP code

## Slide 105: Debugger
Debugger uses exceptions to provide important features:
  Trace—Exception occurs after executing every instruction
  Breakpoints—Interrupted at specific point
Trace mode:
  Exception occurs after the execution of every instruction.
  Debugging program is used as the exception-service routine.
Breakpoints:
  Exception occurs only at specific points selected by the user.
  Debugging program is used as the exception-service routine.

## Slide 106: Privilege exception
Certain instructions can be executed only when the processor is in the supervisor mode. These are called privileged instructions.
If an attempt is made to execute a privileged instruction in the user mode, a privilege exception occurs.
Privilege exception causes
  Processor to switch to the supervisor mode,
  Execution of an appropriate exception-servicing routine.
Notes: Recall privilege mode and supervisor mode. Certain instructions can only be executed in the supervisor mode. If an attempt is made to execute the instruction in the user mode, then an privilege exception occurs. Privilege exception causes the processor to switch to the supervisor mode, and execution of an appropriate service routine.

## Slide 107: Direct Memory Access

## Slide 108: DIRECT MEMORY ACCESS
Drawbacks of previous approaches
Restoring PC and other state information
Processor has to poll IO device/ waits for device to send INT
Transfers large block of data at high speed
  control unit may be provided to transfer a block of data directly between an I/O device and the main memory, without continuous intervention by the processor.

## Slide 109: DIRECT MEMORY ACCESS
Control unit which performs these transfers is part of the I/O device’s interface circuit. This control unit is called as a DMA controller (performs functions of processor).
The requested program will be put in the blocked state.
The operation of the DMA controller must be under the control of a program executed by the processor. That is, the processor must initiate the DMA transfer.
Once the DMA controller completes the DMA transfer, it informs the processor by raising an interrupt signal.

## Slide 110: Direct Memory Access (contd..)
Direct Memory Access (DMA):
  A special control unit may be provided to transfer a block of data directly between an I/O device and the main memory, without continuous intervention by the processor.
Control unit which performs these transfers is a part of the I/O device’s interface circuit. This control unit is called as a DMA controller.
DMA controller performs functions that would be normally carried out by the processor:
  For each word, it provides the memory address and all the control signals.
  To transfer a block of data, it increments the memory addresses and keeps track of the number of transfers.
Notes: This alternative approach is called as direct memory access. DMA consists of a special control unit which is provided to transfer a block of data directly between an I/O device and the main memory without continuous intervention by the processor.
A control unit which performs these transfers without the intervention of the processor is a part of the I/O device’s interface circuit, and this controller is called as the DMA controller.
DMA controller performs functions that would be normally be performed by the processor. The processor will have to provide a memory address and all the control signals. So, the DMA controller will also provide with the memory address where the data is going to be stored along with the necessary control signals. When a block of data needs to be transferred, the DMA controller will also have to increment the memory addresses and keep track of the number of words that have been transferred.

## Slide 111: DMA
To initiate the DMA transfer, the processor informs the DMA controller of:
  Starting address,
  Number of words in the block.
  Direction of transfer (I/O device to the memory, or memory to the I/O device).
R/W =1 Read(MIO)
Done=1 when completed Transfer
IE=1 when ready for next transfer
IRQ=1 when interrupt is requested

## Slide 112: Direct Memory Access
memory
Processor
System bus
Main
Keyboard
Disk/DMA
controller
Printer
DMA
controller
Disk
Disk
DMA controller connects a high-speed network to the computer bus.
Disk controller, which controls two disks also has DMA capability. It provides two
DMA channels.
It can perform two independent DMA operations, as if each disk has its own DMA
controller. The registers to store the memory address, word count and status and
control information are duplicated.
Network
Interface
Notes: Let us consider a memory organization with two DMA controllers. In this memory organization, a DMA controller is used to connect a high speed network to the computer bus. In addition, disk controller which also controls two disks may have DMA capability. The disk controller controls two disks and it also has DMA capability. The disk controller provides two DMA channels. The disk controller can two independent DMA operations, as if each disk has its own DMA controller. Each DMA controller has three registers, one to store the memory address, one to store the word count, and the last to store the status and control information. There are two copies of these three registers in order to perform independent DMA operations. That is, these registers are duplicated.

## Slide 113: Direct Memory Access
Processor and DMA controllers have to use the bus in an interwoven fashion to access the memory.
  DMA devices are given higher priority than the processor to access the bus.
  Among different DMA devices, high priority is given to high-speed peripherals such as a disk or a graphics display device.
Processor originates most memory access cycles on the bus.
  DMA controller can be said to “steal” memory access cycles from the bus. This interweaving technique is called as “cycle stealing”.
An alternate approach is the provide a DMA controller an exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block or burst mode.
Notes: Processor also has to transfer data to and from the main memory. Also, the DMA controller is responsible for transferring data to and from the I/O device to the main memory. Both the processor and the DMA controller have to use the external bus to talk to the main memory. Usually, DMA controllers are given higher priority than the processor to access the bus. Now, we also need to decide the priority among different DMA devices that may need to use the bus. Among these different DMA devices, high priority is given to high speed peripherals such as a disk or a graphics display device.
Usually, the processor originates most cycles on the bus. The DMA controller can be said to steal memory access cycles on from the bus. Thus, the processor and the DMA controller use the bus in an interwoven fashion. This interweaving technique is called as cycle stealing.
An alternate approach would be to provide DMA controllers exclusive capability to initiate transfers on the bus, and hence exclusive access to the main memory. This is known as the block mode or the burst mode of operation.